## Slide 1: MODFLOW 6 Final Items and Current Plans
47TH IAH Congress
São Paulo, Brazil
August 22, 2021
Notes: Describe some of the ongoing work we are doing with MODFLOW
MODFLOW and related software distributed by the USGS is developed and supported by a growing team of USGS scientists and external collaborators. Recent MODFLOW development efforts have focused on use of unstructured and locally refined grids for constant or variable-density groundwater flow and solute transport simulation, robust handling of three-dimensional anisotropy, generalization and tracking of water transfer between packages, distributed memory parallelization, and consolidation of these core capabilities into MODFLOW 6. These capabilities make it possible to construct new types of models, such as tightly coupled nested models, that have not been possible with previous MODFLOW versions. Underlying these efforts has been the adoption of an open-development philosophy that relies on testing-based development and continuous integration practices by the core development team and by the broader MODFLOW community. Ongoing development increasingly relies on the Flopy python package for automating model construction. Resulting from these development efforts is a suite of MODFLOW programs that can be applied at local, regional, and National scales for a wide variety of complex groundwater flow and transport problems.
OASIS MCT

## Slide 2: Current MODFLOW 6 Capabilities
Groundwater Flow (GWF) Model (August 2017)
Compaction and Subsidence (CSUB) Package (December 2019)
Groundwater Transport (GWT) Model (October 2020)
Coupled Variable-Density Flow and Transport (October 2020)
MODFLOW API (June 2020)
Notes: One of the reasons for this presentation is to let you know about some of the new MODFLOW capabilities that have been released recently
We started working on MODFLOW 6 in about 2013.
At that time (and even today) there were lots of different flavors of MODFLOW (2005, USG, NWT, SEAWAT, GWM, ...), and we wanted to bring them together into a cohesive new framework
The idea was to modernize the code and make it easier to couple with other models.

## Slide 3: API for MODFLOW 6
Developed in collaboration with Martijn Russcher, Deltares
Full control of MODFLOW while it’s running
Well-defined interfaces based on Basic Model Interface (BMI) standard
Access to MODFLOW internal variables (as a copy or pointer)
Three different levels of control
  Between time steps (BMI)
  Within a time step
  Within an iteration
Uses identical code base as executable version

## Slide 4: Why We’re Excited about the API!
Tight integration with other models
Callable from other languages, such as Python; access to 3rd party tools
Sensitivity analysis, adjoint state, parameter estimation, optimization, uncertainty analysis
Alternative solvers (PETSc, …)
Alternative data input (netCDF, database access, online services, …)
MODFLOW can be customized by our users
Prevents linkages from becoming stale

## Slide 5: Current Development Plans
Node Property Flow and Storage Package enhancements
  Variable Hydraulic Conductivity and Storage with Depth Capability
  Time-Variant Hydraulic Conductivity and Storage Capability
Agricultural Demand (AG) Package (or API link with other demand models)
SFR n-point cross section as alternative to rectangular channels
Development of a land surface model based on PRMS
Parallelization of multiple coupled models using the Message Passing Interface (MPI)
Particle Tracking (PRT) Model for structured and unstructured grids
Land-surface model based on PRMS (or API link with other LSMs)

## Slide 6
Any Questions?