## Slide 1: MODFLOW 6 Unstructured Grids
47TH IAH Congress
São Paulo, Brazil
August 22, 2021
Notes: Describe some of the ongoing work we are doing with MODFLOW
MODFLOW and related software distributed by the USGS is developed and supported by a growing team of USGS scientists and external collaborators. Recent MODFLOW development efforts have focused on use of unstructured and locally refined grids for constant or variable-density groundwater flow and solute transport simulation, robust handling of three-dimensional anisotropy, generalization and tracking of water transfer between packages, distributed memory parallelization, and consolidation of these core capabilities into MODFLOW 6. These capabilities make it possible to construct new types of models, such as tightly coupled nested models, that have not been possible with previous MODFLOW versions. Underlying these efforts has been the adoption of an open-development philosophy that relies on testing-based development and continuous integration practices by the core development team and by the broader MODFLOW community. Ongoing development increasingly relies on the Flopy python package for automating model construction. Resulting from these development efforts is a suite of MODFLOW programs that can be applied at local, regional, and National scales for a wide variety of complex groundwater flow and transport problems.
OASIS MCT

## Slide 2: MODFLOW 6 Unstructured Grids

## Slide 3: Spatial Discretization
Three ways to enter grid
  DIS – regular MODFLOW grid
  DISV – discretization by vertices
  DISU – fully unstructured

## Slide 4: Unstructured Grids
What do we mean by unstructured?
  1. Cell can be connected to any number of surrounding cells
  2. Not a regular MODFLOW grid
Why use them?
  Grid can conform to irregular model domain boundaries
  Resolution can be added in areas of interest
Why not use them?
  More complicated to work with
  Poor grid design can lead to errors in the flow solution that are difficult to find and quantify

## Slide 5: CVFD Requirements
Connecting line bisects shared edge at right angle
Possible issues
Good

## Slide 6: Types of Unstructured Grids
Rectangular based
  Quadpatch
  Quadtree / Octree
Triangular
Voronoi
Others

## Slide 7: Ghost-Node Correction
Can be used to correct the flow calculation when the CVFD requirement is violated

## Slide 8: XT3D
Sophisticated flow formulation designed to handle full 3D anisotropy
XT3D also improves flow solution for grids that do not honor the CVFD requirements

## Slide 9: XT3D Solution

## Slide 10: Unstructured Grids in MODFLOW 6
Discretization by Vertices (DISV) Package
  New in MODFLOW 6
Unstructured Discretization (DISU) Package
  Patterned after approach in MODFLOW-USG
Multiple models

## Slide 11: “CELLID”
Regular MODFLOW grid (DIS)
  (LAYER, ROW, COLUMN)
Discretization by Vertices (DISV)
  (LAYER, CELL NUMBER)
Unstructured Discretization (DISU)
  (CELL NUMBER)

## Slide 12: DISV package

## Slide 13: Vertices and Cells

## Slide 14: DISU Package

## Slide 15: DISU Connections

## Slide 16: DISU Vertically Staggered Connections
Cell can be connected to more than one cell in a single horizontal direction

## Slide 17: DISU Connection Data
1
2
3
4
5
6
7
8
9

## Slide 18: Local Grid Refinement: Multi-model simulation A compromise….

## Slide 19: Multi-Model Simulation
MODFLOW 6 foundation allows models to be tightly coupled at the matrix level
Allows local grid refinement (LGR), and other model coupling strategies

## Slide 20: LGR Simulation
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2

## Slide 21: GWF Exchanges
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC

## Slide 22: Matrix-Level Coupling
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC
Notes: Because our solver is unstructured and asymmetric, can handle Newton-Raphson, unstructured grids, ghost nodes, XT3D, dispersion tensors, etc…

## Slide 23: QUESTIONS?