## Slide 1: MODFLOW 6 Groundwater Transport Model
University of Neuchâtel, Switzerland
Centre for Hydrogeology and Geothermics
December 16-20, 2019
Notes: Describe some of the ongoing work we are doing with MODFLOW
MODFLOW and related software distributed by the USGS is developed and supported by a growing team of USGS scientists and external collaborators. Recent MODFLOW development efforts have focused on use of unstructured and locally refined grids for constant or variable-density groundwater flow and solute transport simulation, robust handling of three-dimensional anisotropy, generalization and tracking of water transfer between packages, distributed memory parallelization, and consolidation of these core capabilities into MODFLOW 6. These capabilities make it possible to construct new types of models, such as tightly coupled nested models, that have not been possible with previous MODFLOW versions. Underlying these efforts has been the adoption of an open-development philosophy that relies on testing-based development and continuous integration practices by the core development team and by the broader MODFLOW community. Ongoing development increasingly relies on the Flopy python package for automating model construction. Resulting from these development efforts is a suite of MODFLOW programs that can be applied at local, regional, and National scales for a wide variety of complex groundwater flow and transport problems.
OASIS MCT

## Slide 2: MODFLOW 6 groundwater transport model

## Slide 3: Transport Model
New model type in MODFLOW 6 called GWT
  Can run concurrently with GWF, or
  Can run by itself using saved GWF results
Alternative to MT3D
  MT3D-USGS will work with MODFLOW 6 output for regular grids
Works with unstructured grids
Works with the Newton flow formulation
Simulates advection, dispersion, sources and sinks, sorption, decay, and any number of immobile domain
Implicit formulation (no particles)
  Second-order TVD
  Optional use of XT3D for dispersion

## Slide 4: Documentation in Preparation

## Slide 5: Transport Equation

## Slide 6: GWT Packages

## Slide 7: Domain and Package Structure

## Slide 8: Typical GWF-GWT Simulation

## Slide 9: Simulation Name File

## Slide 10: Model Name Files
GWF Name File
GWT Name File

## Slide 11: Limitations
Flow and transport grids must be identical
Time step lengths are specified by the user in the TDIS package
No particle methods
Version 1:
  No transport from one GWT model to another one
  Single species, but can specify multiple GWT models, with each one representing a different species

## Slide 12: Newton Formulation for Dry Cells
Qrch
1
2
3
h1
h2
h3

## Slide 13: Transport Formulation for Dry Cells
QrchCrch
1
2
3
C1 = Crch
C2 = Crch
C3 = f(Crch, …)

## Slide 14: Keating Example
Transport through dry cells

## Slide 15: SEAWAT Capabilities
Simulated concentrations can be used to calculate densities used by the GWF Buoyancy Package
Flow and transport can be solved in a single matrix (more to do on this…)
Compatible with unstructured grids and the Newton flow formulation

## Slide 16: Freshwater Head Formulation
SEAWAT uses a freshwater head formulation
Problem: freshwater head is not the water table
Notes: q = - K_0 \left [ \nabla h_f + \left ( \frac{\rho}{\rho_0} - 1 \right ) \nabla z \right ]

## Slide 17: Alternative Hydraulic Head Formulation
What about a hydraulic head formulation?
Head is the dependent variable and the water table
Notes: q = - K_0 \left [ \nabla h_f + \left ( \frac{\rho}{\rho_0} - 1 \right ) \nabla z \right ]

## Slide 18: Hydraulic-Head Formulation Manuscript

## Slide 19: MODFLOW 6 Animation
Notes: 10 seconds to run this.

## Slide 20: Elder-Like Problem

## Slide 21: Unstructured Cross-Section Simulation

## Slide 22: Examples Document

## Slide 23: QUESTIONS?