## Slide 1: MODFLOW 6 Groundwater Flow Model
47TH IAH Congress
São Paulo, Brazil
August 22, 2021
Notes: Describe some of the ongoing work we are doing with MODFLOW
MODFLOW and related software distributed by the USGS is developed and supported by a growing team of USGS scientists and external collaborators. Recent MODFLOW development efforts have focused on use of unstructured and locally refined grids for constant or variable-density groundwater flow and solute transport simulation, robust handling of three-dimensional anisotropy, generalization and tracking of water transfer between packages, distributed memory parallelization, and consolidation of these core capabilities into MODFLOW 6. These capabilities make it possible to construct new types of models, such as tightly coupled nested models, that have not been possible with previous MODFLOW versions. Underlying these efforts has been the adoption of an open-development philosophy that relies on testing-based development and continuous integration practices by the core development team and by the broader MODFLOW community. Ongoing development increasingly relies on the Flopy python package for automating model construction. Resulting from these development efforts is a suite of MODFLOW programs that can be applied at local, regional, and National scales for a wide variety of complex groundwater flow and transport problems.
OASIS MCT

## Slide 2: GROUNDWATER MODELING background AT THE USGS

## Slide 6
Notes: I sometimes show this slide that I received from Lenny Konikow to give some historical context about MODFLOW. This is an internal USGS memo from John Bredehoeft in 1979 that gives the marching orders to begin developing MODFLOW. There are a few important things to note here: (1) this was 40 years ago! (2) the model should be machine independent, flexible, and teachable, Modules are independent of one another!

## Slide 8: MODFLOW Philosophy
Core Principles
Teachable
Documented
Reliable
Robust
Efficient
Extensible
Portable
Notes: I was lucky to have the opportunity to work with Arlen Harbaugh for a couple of years. Arlen is one of the original developers of MODFLOW. Arlen saw MODFLOW as more than just a program. MODFLOW was the philosophy before a number of core principals: …. Many believe these core principals are behind MODFLOW’s popularity. We are here 40 years later at the MODFLOW conference.

## Slide 9: MODFLOW Support Environment
Core Principles
Teachable
Documented
Reliable
Robust
Efficient
Extensible
Portable
Groundwater Vistas GMS Visual MODFLOW. PMWIN ModelMuse Groundwater Desktop Leapfrog Hydro FREEWAT iMOD ModelViewer FloPy Graphical Interfaces and Scripting
Notes: Because of it’s popularity, a wide variety of tools have been developed to support MODFLOW…

## Slide 10
Reactive
Transport
Solute and Heat
Transport
Landscape
Hydrology
Parallel
Subsidence
Unstructured
Grids
Parameter
Estimation
and Uncertainty
Unsaturated
Zone
Karst and
Pipe Flow
Flow Path
Analysis
Management
Surface Water
Flow
Core Principles
Teachable
Documented
Reliable
Robust
Efficient
Extensible
Portable
Groundwater Vistas GMS Visual MODFLOW. PMWIN ModelMuse Groundwater Desktop Leapfrog Hydro FREEWAT iMOD ModelViewer FloPy Graphical Interfaces and Scripting
Notes: Over the years, our groundwater problems have become more and more complex. As hydrogeologists and scientists , we are being asked to address karst problems, transport problems, unsaturated zone problems, etc. As a result, MODFLOW has been expanded to incorporate other processes and coupled with a variety of other models.

## Slide 11
MODPATH
mod-PATH3DU
PATH3D
FlowSource
MODFLOW-USG
CFP, VKD
PESTPP-OPT
MODSIM
GWM
UZF
HYDRUS
VSF
SFR, SWR
HEC-RAS
BRANCH
PEST
PESTPP
UCODE
MODFLOW-USG
MODFLOW 6
SUB
CSUB
SAMG
PKS-MODFLOW
PKS-SEAWAT
MODFLOW 6
GSFLOW-PRMS
SWB, HSPF, SWAT
OWHM
MT3DMS
MT3D-USGS
SEAWAT, SWI
GWT
PHREEQC-PHT3D
PHWAT
RT3D
MODFLOW
ECOSYSTEM OF CODES
Groundwater Vistas GMS Visual MODFLOW. PMWIN ModelMuse Groundwater Desktop Leapfrog Hydro FREEWAT iMOD ModelViewer FloPy Graphical Interfaces and Scripting
Reactive
Transport
Solute and Heat
Transport
Landscape
Hydrology
Parallel
Subsidence
Unstructured
Grids
Parameter
Estimation
and Uncertainty
Unsaturated
Zone
Karst and
Pipe Flow
Flow Path
Analysis
Management
Surface Water
Flow
Core Principles
Teachable
Documented
Reliable
Robust
Efficient
Extensible
Portable
Notes: This slide, which is surely incomplete, shows a MODFLOW ecosystem in which many different packages, processes, and codes have been written or coupled to solve these problems. This is an impressive collection of capabilities that use MODFLOW in one way or another.

## Slide 12: MODFLOW User Base
Academics
Private Consultants
Local, State, and Federal Government
MODFLOW and More Conference
Notes: Most groundwater availability studies used MODFLOW

## Slide 13: Evolving Simulation Needs
GW issues becoming more complex
Proliferation of new versions and packages
Increase in package complexity
Loss of package independence
Incompatibilities
Difficult to add other process models to MODFLOW; same grid required for all packages and processes
Notes: ----- Meeting Notes (8/13/15 09:29) -----
GW-SW interaction
Watershed hydrology
Geomechanical issues with subsidence
Chemistry
Management

## Slide 14: MODFLOW Next Generation
2013 Office of Groundwater initiated a major MODFLOW revision
Rewrote MODFLOW using an object-oriented design
Consolidated capabilities from previous MODFLOW versions
Changed name from “Modular Groundwater Model” to “Modular Hydrologic Model”
Published MODFLOW 6 in 2017
Try to follow modern software design principles

## Slide 15: MODFLOW 6
Consolidate popular capabilities from previous MODFLOW versions (2005, NWT, USG, LGR, …)
Improve solution technique
Modernize code and input structure
Support multi-model simulations
Extend MODFLOW into a hydrologic simulator
New core version (Released August 2017)
1984
1988
1996
2000
2005
2017
Notes:     MODFLOW 6 will combine the best features of existing versions of MODFLOW and get rid of outdated functionality. Highly coupled and complex systems will be solved with one system of equations making this MODFLOW version much faster than with previous versions of MODFLOW that iteratively solved the flow part, then the other parts, like transport or local grid refinement. This effort intends to modernize MODFLOW’s design to account for 20+ years of improvements in software design and essentially making MODFLOW a more of a hydrologic simulator.

## Slide 16: MODFLOW 6
Notes: Our group is charged with developing and maintaining the USGS MODFLOW program. This is includes MODFLOW-2005, MODFLOW-NWT, MODFLOW-USG, SEAWAT, and others. In 2017 we released MODFLOW 6 as a new version of MODFLOW that we could use to build from.

## Slide 17: MODFLOW 6 Framework

## Slide 18: MODFLOW 6 Framework Concepts
Simulation
Solution
Model
Packages
Exchanges
Notes:   Groundwater Flow
  Transport
  Pipe Network
  Surface Water Flow
  Landscape Hydrology

## Slide 19: MODFLOW Framework Components
MODFLOW-2005
MODFLOW 6

## Slide 20: Nested Grids
Parent
Child 2
Grandchild
Child 1

## Slide 21: Multi-Level Grid Nesting
Notes: Large scale and fine scale

## Slide 22: MODFLOW 6 Framework
Advantages
  Models are independent
    Models can have their own resolution
    Models can be developed separately
    Models can run independently
  Models can be tightly coupled at the matrix level
  Input and output is standardized
  Model / package approach is highly modular and extensible
  Platform independent, can run on a supercomputer or a Raspberry Pi
Disadvantages
  Models must be programmed to work in the framework
  Framework primarily tested for groundwater
  Framework has been applied to models with an implicit formulation
  Framework requires dedicated maintenance and support

## Slide 23: MODFLOW 6 Framework Simulation Components
Timing Module
Solutions
Models
Exchanges
Utilities
Simulation
Solution 1
Model 4
Timing Module
Model 1
Model 3
Model 2
Exchange 1
Exchange 2
Exchange 3

## Slide 24: MODFLOW 6 Framework Simulation Name File
Required even for common case with one model
Named mfsim.nam
One simulation per folder

## Slide 25: MODFLOW 6 Framework Timing Module
TDIS Package
  Uses the MODFLOW concepts of stress periods, time steps
Alternative timing packages may be developed in the future
Timing applies to all models

## Slide 26: MODFLOW 6 Framework Stress Period Data
Stress are active until changed by the user
  Different from previous MODFLOW versions
Can be specified using time series
BEGIN OPTIONS
PRINT_INPUT
PRINT_FLOWS
SAVE_FLOWS
END OPTIONS
BEGIN DIMENSIONS
MAXBOUND 42
END DIMENSIONS
BEGIN PERIOD 1
# canal
1 1 1 330.0
1 2 1 330.0
1 3 1 330.0
1 4 1 330.0
...
# river
1 1 20 320.0
1 2 20 320.0
1 3 20 320.0
...
END PERIOD

## Slide 27: MODFLOW 6 Framework Solutions
Used to solve one or more models and exchanges
The only solution available now is the Iterative Model Solution, or IMS
  Unstructured and asymmetric
IMS solves the following nonlinear equation
  Ax = b

## Slide 28: Iterative Model Solution (IMS6)

## Slide 29: MODFLOW 6 Framework Time Series
tides.ts
GHB Input File

## Slide 30: Timeseries Interpolation Methods
STEPWISE
  Values are constant until changed
LINEAR
  Average value is calculated for the time step
LINEAREND
  Value interpolated at end of time step

## Slide 31: MODFLOW 6 Framework Observations
OBS Package for GWF Model
  Heads
  Flow between cells
Separate OBS files for each package

## Slide 32: Groundwater flow (GWF) model

## Slide 33: GWF Documentation

## Slide 34: GWF Model Highlights
Generalized control-volume finite-difference formulation
  Regular MODFLOW grids
  Unstructured grids
IDOMAIN capability
Full 3D anisotropy
Multiple stress package ”instances”
Block and keyword input structure

## Slide 35: UNDERLYING Formulation

## Slide 36: Finite-Difference Equation

## Slide 37: Generalized CVFD Equation

## Slide 38: DISCRETIZATION

## Slide 39: Spatial Discretization
Three ways to enter grid
  DIS – regular MODFLOW grid
  DISV – discretization by vertices
  DISU – fully unstructured

## Slide 40: Discretization (DIS) Package
“Regular MODFLOW grid”
Consists of layers, rows, and columns
Top and bottoms can have variable elevations

## Slide 41: IDOMAIN Capability
Improve efficiency for models with large areas of inactive cells
Address MODFLOW limitations with discontinuous hydrogeologic layers

## Slide 42: IDOMAIN Capability (cont.)
Permanently remove a cell from the simulation
Can be used with DIS and DISV
Optionally connect overlying and underlying cells

## Slide 43: Multi-Model Simulation
MODFLOW 6 foundation allows models to be tightly coupled at the matrix level
Allows local grid refinement (LGR), and other model coupling strategies

## Slide 44: LGR Simulation
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2

## Slide 45: GWF Exchanges
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC

## Slide 46: LGR Simulation
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC
BEGIN OPTIONS
END OPTIONS
BEGIN TIMING
TDIS6 mysim.tdis
END TIMING
BEGIN MODELS
GWF6 parent.nam PARENT
GWF6 c1.nam C1
GWF6 c2.nam C2
GWF6 gc.nam GC
END MODELS
BEGIN EXCHANGES
GWF6-GWF6 parent-c1.exg PARENT C1
GWF6-GWF6 parent-c2.exg PARENT C2
GWF6-GWF6 c1-gc.exg C1 GC
END EXCHANGES
BEGIN SOLUTIONGROUP 1
IMS6 mysolver.ims PARENT C1 C2 GC
END SOLUTIONGROUP
Simulation Name File

## Slide 47: Matrix-Level Coupling
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC
Notes: Because our solver is unstructured and asymmetric, can handle Newton-Raphson, unstructured grids, ghost nodes, XT3D, dispersion tensors, etc…

## Slide 48: GWF6-GWF6 Exchange

## Slide 49: NODE PROPERTY FLOW PACKAGE

## Slide 50: Node Property Flow (NPF) Package
Primary purpose is to calculate conductance between adjacent cells
  Confined or convertible cells (ICONVERT)
  Homogeneous or heterogenous
  Isotropic or anisotropic
Handles wetting and drying (REWET, WETDRY) (still available, but the Newton-Raphson method is much better)
Can calculate the three components of specific discharge at the cell center (SAVE_SPECIFIC_DISCHARGE). Nice for vector plots, and required for transport.

## Slide 51: Representation of Anisotropy
Representation of full 3D anisotropy may be required for some problems (fractured aquifers, structurally deformed aquifers)
Some capabilities available (LVDA, SUTRA), but needed generalized CVFD method

## Slide 52: Hydraulic Conductivity Ellipsoid
Defined by three user-provided values on a cell by cell basis
For unrotated case,
  K11 = Kx
  K22 = Ky
  K33 = Kz
K11
K22
K33

## Slide 53: Ellipsoid Rotation
Users can optionally provide ANGLE1, ANGLE2, and ANGLE3 on a cell by cell basis
ANGLE1 is counter-clockwise rotation in the x, y plane

## Slide 54: Ellipsoid Rotation (cont.)
All three angles can be specified to represent ellipsoid orientation

## Slide 55: Effective Conductivity Approach
Large errors for certain ellipsoid configurations
Approximate, but relatively fast
Simple to implement

## Slide 56: XT3D Approach
General and robust handling of anisotropy
Computationally expensive
Improves flow solution for certain grid types
  More on this later

## Slide 57: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells

## Slide 58: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells

## Slide 59: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells

## Slide 60: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells

## Slide 61: XT3D flow expression
Flow between two cells expressed in terms of conductance-like coefficients that can involve all neighbors of the two cells
Larger stencil than in standard conductance-based MODFLOW formulation

## Slide 62: XT3D performance
Longer run times than standard MODFLOW formulation
Requires more memory than standard MODFLOW formulation
“RHS” suboption makes memory requirement comparable to default formulation (same stencil)

## Slide 63: Newton-Raphson Formulation

## Slide 64: Formulation Issues
Originally developed for groundwater flow problems with standard boundary conditions to solve linear (confined) to well-behaved non-linear (unconfined) problems.
Empirical wetting and drying approach added by McDonald and others (1992) to allow cell conversion to simulate more difficult unconfined problems.
Three-dimensional unconfined applications and head-dependent stress packages can create additional nonlinearities.

## Slide 65: Wetting/Drying Nonlinearities
Standard Formulation approach:
Dry cells are inactivated. This creates discontinuities and oscillations. Furthermore, wetting/drying results in varying stresses (for example, wells disappear from dry cells).
Newton-Raphson Formulation approach:
Keep all cells active even when the head in a cell is below the bottom of the cell

## Slide 66: Newton-Raphson method
http://tutorial.math.lamar.edu/Classes/CalcI/NewtonsMethod.aspx
Newton-Raphson:
Standard Formulation:
Jacobian:
Modified Newton-Raphson:

## Slide 67: Newton-Raphson Formulation
Conductance transitions from head-dependent to constant
Transition causes to change from 1 to zero, a discontinuous derivative
Cell
bottom
Cell
top
0

## Slide 68: Newton-Raphson Formulation
Smooth saturated thickness function over the discontinuity.

## Slide 69: Standard Formulation
Standard Formulation intercell conductance based on saturated thickness will prevent flow from a wet cell to a dry cell.
dry
hn = 90
SFn = 0
BOTn = 90
wet
hm = 95
SFm = 5
BOTm = 90

## Slide 70: Newton-Raphson Formulation
Conductance is calculated based on saturated thickness of cell with higher head. Thus, there will be flow from the wet cell to the dry cell.
dry
hn = 90
SFn = 0
BOTn = 90
hm = 95
SFm = 5
BOTm = 90
wet

## Slide 71: Newton-Raphson Formulation
Since cells remain active, simulated heads can be less than the cell bottom.

## Slide 72: Newton-Raphson Formulation
Under-relaxation for Newton Solutions

## Slide 73: Newton-Raphson Formulation
Once Newton-Raphson is enabled in the GWF name file Newton-Raphson is also used for GWF terms formulated by
Storage Package
Well Package (auto flow reduce)
Lake Package*
Multi-aquifer Well Package
Streamflow Routing Package*
Unsaturated Zone Flow Package*
* Stress package continuity equation also solved using Newton-Raphson

## Slide 74: Newton-Raphson Formulation
Newton-Raphson formulation is more robust than Picard for strongly non-linear problems.
Newton-Raphson formulation results in a asymmetric matrix.
Asymmetric matrix requires different linear accelerators, line search methods, and under-relaxation methods

## Slide 75: Iterative Model Solution (IMS6) Package
Nonlinear methods
Backtracking
Under-relaxation Methods
  Simple (equivalent to MODFLOW-2005 PCG package under-relaxation)
  Cooley
  Delta-Bar-Delta
Pseudo-Transient Continuation for steady-state Newton-Raphson problems

## Slide 76: Newton-Raphson Formulation
Zaidel, Jacob, 2013, Discontinuous steady-state analytical solutions of the Boussinesq equation and their numerical representation by MODFLOW: Groundwater, v. 51, p. 952–959. doi: 10.1111/gwat.12019.

## Slide 77: Newton-Raphson Formulation
Keating, Elizabeth, and Zyvoloski, George, 2009, A stable and efficient numerical algorithm for unconfined aquifer analysis: Ground Water, v. 47, no. 4, p. 569–579, accessed June 27, 2017, at https://doi.org/10.1111/ j.1745-6584.2009.00555.x.

## Slide 78: storage

## Slide 79: Storage (STO) Package
Steady state if STO Package not specified for a simulation
Cells are treated as confined or convertible (ICONVERT)
Aquifer storage properties (SS and SY) are specified
Individual stress periods are marked as steady state or transient

## Slide 80: Skeletal Storage, Compaction and Subsidence (Csub) Package

## Slide 81: Previous subsidence package versions

## Slide 82: CSUB Package – Capabilities
Package based on MODFLOW-2005 SUB and SUB-WT Packages
Effective stress formulation
  Effective stress dependent storage properties
  Water table dependent compaction
Elastic and inelastic compaction of fine-grained sediments
  No-delay (thin beds that equilibrate quickly)
  Delay (thick beds that drain slowly – separate numerical solution)
Can account for elastic compaction of coarse-grained aquifer materials and water compressibility (full storage equation)

## Slide 83: CSUB Package – theory
Assuming compaction is predominantly vertical
where

## Slide 84: CSUB Package – theory

## Slide 85: CSUB Package – input

## Slide 86: CSUB Package – input options
Head-based formulation
Compaction dependent porosity/void ratio and thickness for no-delay beds
Specify interbed thickness as a fraction of cell thickness
Time-varying geostatic stress above model

## Slide 87
One-dimensional column problem simulating extensometer observations
Sneed (2008) model used head-based formulation (SUB package)
Combination of no-delay and delay interbeds
Elastic compressibility of coarse-grained materials and water compressibility simulated
Specified water-levels used to simulate historic water-level changes
Calibrated using PEST++
  Calibrated to simulated compaction from head-based results
  Calibrated inelastic specific storage with tied elastic specific storage and original multiplier
  Coarse-grained elastic specific storage insensitive

## Slide 89: Traditional stress packages

## Slide 90: Traditional Packages
Specified head (CHD) Package
  No more IBOUND. Must use CHD
  Can turn CHD cells on and off by stress period
Well (WEL) Package
Recharge (RCH) Package
  Array-based or list based
River (RIV) Package
General-Head Boundary (GHB) Package
Drain (DRN) Package
Evapotranspiration (EVT) Package
  Array-based or list based

## Slide 91: All GWF Packages

## Slide 92: Multiple Package of Same Type

## Slide 93: QUESTIONS?